## Slide 1
5G Technology Tutorials
Zhu Han
Department of Electrical and Computer Engineering
University of Houston, Houston, TX, USA
Slides on http://wireless.egr.uh.edu/research.htm

## Slide 2: Table of Content
Overview of 5G
Key Technologies
  Device-to-device Communication
  Small Cell Network (HetNet)
  Full Duplex

## Slide 3: Standardization Facilitates Technology Evolution
2015
2005
2000
1995
2010
Each new evolution builds on the established market of the previous
Backwards-compatible evolution
But larger technology steps require revolutions:
From TDMA:
to CDMA:
to OFDMA:

## Slide 4: KPIs 6 Key Performance Indicators (KPIs) for 5G
Chart: 
| 2010 | 2011 | 2012 | 2020
系列 1 | 1 | 2 | 4 | 20
1000X Capacity
(Traffic and Connections)
10Gbps
10X Peak Data Rate
(10+Gbps)
10X User Rate Anywhere
(100M-1Gbps)
1000X Energy&Cost Reduce
10X Low Latency,
High reliability
But what is 5G? D2D, small cell, Massive MIMO or full duplex?
5-10X Spectrum Efficiency

## Slide 5: Future Wireless Challenges
Mobile Internet and Smart Phones
  Bandwidth and data traffic boost (Cisco)
    Data traffic increases 2 times/per year, 1000 times by 2020
    Wireless network cannot support that!
  Information aggregate to hotspot and local area
    70% in office and hotspot, over 90% in future
    Hotspot QoS cannot be guaranteed!
  Bandwidth demand over 1200MHz，ITU assignment less than 600MHz

## Slide 6: Table of Content
Overview of 5G
Key Technologies
  Device-to-device Communication
  Small Cell Network (HetNet)
  Full Duplex

## Slide 7: Possible Solutions
Number of UE
Cell Capacity
Add fixed AP
Sum rates
P. Gupta and P. Kumar, “The capacity of wireless networks,” IEEE Transactions on Information Theory, vol. 46, no. 2, pp. 388-404, Mar. 2000.
Ad-hoc opti-mal rate
By “Shannon Theory”，network capacity relies on bandwidth and APs
Current：Add fixed APs
Combine Cellular and Ad-hoc

## Slide 8: Definition and Benefits
Definition of Device-to-Device (D2D) Communications
  D2D communications commonly refer to the technologies that enable devices to communicate directly without an infrastructure of access points or base stations.
eNB
eNB
Increase network capacity
Extend coverage
Offload data
Improve energy efficiency
Create new applications

## Slide 9: Deployment Roadmap
Cellular unaware D2D
Cellular network is not aware of D2D
2 RATs, e.g. 3G + Wifi
No cooperation between cellular and D2D
Cellular aware D2D
Cellular network is aware of D2D
2 RATs, e.g. LTE + Wifi
Kind of cooperation between cellular and D2D
Cellular controlled D2D
Cellular network fully controls D2D
A single RAT, e.g. LTE-A
D2D is a part of cellular communication
RAT1
RAT2
UE1
UE2
flow1
flow2
Scenario A
RAT1
RAT2
UE1
UE2
flow1
flow2
Scenario B
RAT1
UE1
UE2
flow1
flow2
Scenario C
D2D Benefits Scenario A Scenario B Scenario C
Traffic offload
Unified & Simplified comm.
User experience improvement
Cellular capacity enhancement
RATs converging

## Slide 10: Scenario A: Cellular Unaware
App
3G
3G
Wifi
Wifi
Example structure:
App
New App
Typical applications
  Data synchronization, Social networking, Mobile advertising, Automation control, etc.
BS
BS
social network
Data synchronization
Mobile advertising
Key technology
  D2D opportunity identification & neighbor discovery
  Flow distribution among different RATs
  Cognitive radio technology
Benefits/Gains
  Offload cellular traffic
  Unified & Simplified communications
Node functionality
  User device: application distribute flows among different RATs
  No impact on RAN & CN nodes

## Slide 11: Scenario B: Cellular aware
App
LTE
LTE
Wifi
Wifi
Example structure:
App
Core Network
New coordination function/services
Key technology
  D2D opportunity identification
  D2D coordination
Benefits/Gains
  Better user experience, e.g. QoS, mobility, etc.
  Core network traffic offload
  Unified & Simplified communications
Node functionality
  User device: new D2D coordination function
  RAN node: No impact
  CN node: new D2D coordination function
Typical applications
  Cellular P2P: A, B, C receive data from CN, and share the non-achieved data among themselves
NB
NB
A
B
C
Core Network
CN node

## Slide 12: Scenario C: Cellular controlled
App
Cellular
Example structure:
App
Core Network
New Cellular D2D interface
New D2D control function/services
Typical applications
  Cooperative transmission: Mobiles interact to jointly transmit and/or receive information in cellular environments.
Node functionality
  User device: New D2D control & interface
  RAN nodes: New D2D control function
  CN nodes: New D2D control function
Benefits/Gains
  Cellular capacity improvement
  Better QoS, security & mobility support
  Core network traffic offload
  Unified & Simplified communications
Key technology
  D2D control
  D2D air interface design
  Cooperative transmission
eNB

## Slide 13
D2D Local Area Networks
eNB
eNB
Mobile social networks:
Mobile + social
Connected via mobiles
Information push, sharing, etc
New business model
RAT | Solution | Benefits | Frequency | Disadvantages
Wireless Mesh | WLAN + Ad Hoc | Flexible | Un-authorized | QoS in-guaranteed
D2D LAN | Cellular +Ad Hoc | Flexible | Authorized | QoS guaranteed
Smart-phones and data-service based mobile internet
Wireless Mesh
D2D LAN
UEs can be connected in an Ad-hoc way and use cellular frequency with guaranteed QoS
Create new services for operators and vendors
Expand to many other areas

## Slide 14: D2D LAN System
D2D LAN Protocol
D2D
MME
S-GW
EPC
E-UTRAN
D2D LAN:
Subnet
Parallel to Cellular
Flexible topology
Controlled by core network and eNB
Cellular
System configuration | 
Frequency | Authorized
System | TDD
Network | Cellular network and D2D LAN
UE mode | Cellular/D2D
Topology | Multi-cell
Control | Core network, eNB, and UE
Key issues
Usage scenarios, services, and billing
Channel model
Physical layer
MAC layer
Network layer

## Slide 15: D2D LAN Problems
Realize full connection，networks become complicated
Support high-date transmission，interference becomes severe
Realize four dimension optimization，resource management is challenging
MME
S-GW
Core Net
D2D LAN
Cellular
Introduce“device”freedom
Space, Time, Frequency, and Device, joint optimization
Communication Freedom increase

## Slide 16
Drastically different requirements
The LTE platform would have the advantage over others, such as Wi-Fi and Bluetooth that operate device to device protocols, because they use license exempt spectrum.
Proximity-based applications and services represent a recent and enormous social-technological trend
  These applications and these services are based on the awareness that two devices or two users are close to each other
  Awareness of proximity carries value, and generates demand for an exchange of traffic between them
Direct D2D communication is also essential for public safety services
  e.g. in case of lack of network infrastructure in disaster situations)
3GPP has imitated work on enhancing the LTE-EPC platform to support these capabilities
3GPP R12 on D2D

## Slide 17: Table of Content
Overview of 5G
Key Technologies
  Device-to-device Communication
  Small Cell Network (HetNet)
  Full Duplex

## Slide 18: Overview of Femtocells
Femtocells are low-power wireless access points that operate in licensed spectrum to connect standard mobile devices to a mobile operator’s network using residential DSL or cable broadband connections.

## Slide 19: Overview of Femtocells
Why femtocells is needed?
  Exponentially increasing wireless data traffic.

## Slide 20: Overview of Femtocells
The key attributes of femtocells:
  Mature mobile technology
  Operating in licensed spectrum
  Generating coverage and capacity
  Using internet-grade backhaul
  At competitive prices
  Fully managed by licensed operators
Question
  What is the difference from WIFI: some control
  What is different from microcell: backhaul

## Slide 21: A Brief History of Femtocells
Femtocell ecosystem

## Slide 22: Femtocell Standardization
The governing body for standardization is the Femto Forum (www.femtoforum.org).

## Slide 23: Femtocell Standardization
Mission:
  The mission is to advance the development and adoption of small cells for the provision of high-quality 2G/3G/4G coverage and services within residential, enterprise, public and rural access markets.
3G or 4G
The Femto forum is active in two main areas:
  Standardization, regulation & interoperability;
  Marketing & promotion.

## Slide 24: Femtocell Standardization
Working groups
  The marketing & promotion group
  The radio & physical layer group
  The networks & interoperability group
  The regulatory group

## Slide 25: Femtocell Standardization
3GPP standards for UMTS femtocells
  Interface between the femtocell (Home Node B - HNB) and the femto network gateway (HNB Gateway, HNB-GW)
  Security protocols to authenticate femtocell (HNBs) and secure communications across the un-trusted Internet
  Management protocols for “touch free” Operations, Administration, and Management (OA&M) of femtocells (HNB devices)

## Slide 26: Femtocell Standardization
3GPP2 standards for CDMA femtocells
  SIP/IMS-based 1x circuit services architecture
  Packet data architecture
  Security framework
  Enhancements to mobile devices to make them more femto-aware
  Foundations of femtozone services (Local IP Access and Remote IP Access)
  Femtocell management architecture

## Slide 27: Femtocell Standardization
The need for LTE femtocells
  There is a limit to how many outdoor cell sites can be built;
  The spectrum available to any particular operator is limited;
  Cell site backhaul is expensive.
LTE is the first cellular technology which will be able to take full advantage of femtocell.
  The large quantity of dynamically allocated time and frequency slots.

## Slide 28: Femtocell Standardization
LTE architecture with deployed HeNB GW

## Slide 29: Femtocell Models
Traditional hexagonal grid model
  Dozens of systems parameters can be modeled;
  Other-cell interference can be modeled simply;
  The results is sufficiently accurate to enable the evaluation of new proposed techniques.
Multi-tiered cellular model
  Macrocells
  Picocells
  Femtocells
  Possibly further radiating elements

## Slide 30: Femtocell Models
Link level modeling
  Channel status depend on a large number of factors
    The propagation environment
    Range & distance
    Carrier frequency
    Antenna placement
    Antenna type
The channel behavior of femtocell channels is similar to WiFi channels.
  Indoor, Winner II channel

## Slide 31: Femtocell Models
System level model
  Multi-tiered networks models begin with a spatial point process to statistically model the base station locations of each tier.
The simplest and best known such point process is the Poisson point process.
  The base station positions are all independent which allows substantial tools to be brought to bear from stochastic geometry.

## Slide 32: Femtocell Models
System level model

## Slide 33: Femtocell Models
Femtocell access control model
  Closed subscriber group (CSG)
    Only pre-registered mobile users can use a certain femtocell.
  Open subscriber group (OSG)
    Any mobile can use any femtocell or at least one that is “open”.

## Slide 34: Femtocell Models
Femtocell network model
  Keep the grid model for macro base stations, drop femtocells “on top” of it, either randomly or in a deterministic fashion;
  Focus on a single femtocell dropped in the cellular network;
  Drop both the macrocells and femtocells randomly;
  Keep all the channel gains and possibly even the various per-user capacities general, without specifying the precise spatial model for the various base stations.

## Slide 35: Overview of Key Challenges
Technical challenges
  Interference scenario relationships

## Slide 36: Overview of Key Challenges
Technical challenges
  Interference coordination
    3G CDMA femtos
      power control strategies
      Reserving a “femto-free” band
    4G LTE femtos
      Backhaul-based coordination
      Dynamic orthogonalization
      Subband scheduling
      Adaptive fractional frequency reuse

## Slide 37: Overview of Key Challenges
Technical challenges
  Cell association and biasing
    Biasing: users are actively pushed onto small cells.

## Slide 38: Conclusion
Demand for cellular data services skyrockets
Femtocell
  Organic plug-and-play deployment
  Highly democratic cost
  Possible chaos to the network
Forecast
  Dense femtocell deployment
  Economic and capacity benefit

## Slide 39: Table of Content
Overview of 5G
Key Technologies
  Device-to-device Communication
  Small Cell Network (HetNet)
  Full Duplex

## Slide 40: Background of Full-Duplex Techniques
Traditional half duplex: using orthogonal resources
  Time-division duplex
  Frequency-division duplex
Problems
  The orthogonal resources are allocated for reception and transmission.
Solutions
  The same resources are allocated for reception and
  transmission
Time-division duplex
Frequency-division duplex
Spectral loss
Full-duplex
Comms

## Slide 41: Full Duplex Introduction
A full duplex system allows communication at the same time and frequency resources.
Advantages
  High spectral efficiency
    Same time & same frequency band
  Low cost
    Readily use the existing MIMO radios
    Hardware advancement, etc.
: Signal of interest
: Self interference
Full duplex communication

## Slide 42: Main Challenges
Traditional Challenges
  Very large self interference
    50-110dB larger than signal of interest
    Depending on inter-node distance
  ADC is the bottleneck
    Limited dynamic range: saturation distortion.
    Limited precision: signal of interest is less than noise.
      1 bit ADC is 6 dB in SNR
      Self interference costs 8-18 bits
Need to reduce interference before ADC
Fig. 6 Very large Self interference
Self interference
Received signal
Signal of interest
Fig. 7 Signal after quantization

## Slide 43: Self-interference Cancellation
Self interference channel
Passive antenna propagation suppression
Active cancelation
  Active analog cancelation
  Active digital cancelation
Pre-mixer Post-mixer

## Slide 44: Passive Propagation Cancellation
MIMO system
  Example, two transmitting antenna has 180 degree difference at the receiving antenna
  Multiple antenna for beamforming, nulling and self-interference cancellation.
  Challenges: Narrow band.
  For wideband, wavelength is different,
  so the cancellation is not good

## Slide 45: Active Analog Cancelation (2)
Post-mixer
Post-mixer
Post-mixer
Pre-mixer
ADC
DAC
x
x
Post-mixer

## Slide 46: Active Digital Cancelation
Conceptually simpler – requires no new “parts”
Two-step cancellation:
  Estimate the self residual interference channel hRI through training symbols
  Cancel hRIx[n] at baseband
Useless if interference is too strong (ADC bottleneck)

## Slide 47: Resource Allocation Problem Summary (1)
Mode Switch
  Half-duplex radio
    Due the limited size of transmitter and receiver, many wireless communication systems suffer from the spatial correlation which degrades the performance gain of HD mode.
  Full-duplex radio
    It allows a node to send and receive signals at the same time in the same frequency band.
    However, it is practically impossible to have perfect self interference cancelation, and thus, the amount of RSI greatly affects the performance of FD system.
    As a result, in some scenarios, the HD mode may outperform the FD mode for certain RSI values.
This motivates the adaptive mode switching between the FD and HD modes based on the RSI and channel conditions

## Slide 48: Numerical Results and intuition
Bias: connection to FAP and BS
Backhaul constraint
Switch between HD and FD
Human brain is full duplex, but sometime it is better to be half duplex…
Notes: It is expected that by increasing the spatial correlation coefficients between antennas that the HD performance will degrade.
However, FD performance is independent of the spatial correlation between the antennas.
It can be clearly noticed that the proposed scheme was able to switch between FD and HD to choose the transmission mode with the highest throughput

## Slide 49: Resource Allocation Problem Summary (2)
Power Control
  due to RSI, power control algorithm needs to be properly redesigned in order to maximize system performance of all users.
    FD-MIMO:
      The antennas at the FD node are divided into transmit and receive antenna sets
      Water-filling power allocation can be applied at the transmit antenna set to maximize the sum rate based on individual power constraint.
    FD-Relay:
      In FD-Relay networks with individual power constraint at each relay, the relayed signals are corrupted by the RSI,
      Power allocation can be considered to reduce RSI subject to total and individual power constraints

## Slide 50: Resource Allocation Problem Summary (3)
Power Control
  FD-OFDMA: for FD-OFDMA with one FD BS and HD multiple users, uplink (transmit) and downlink (receive) users are paired to communicate with FD BS at the same time.
    The transmit power can be allocated at the BS side with total power constraint by splitting the power among all he subcarriers for different user pairs.
    At the user side, power control needs to take into account the inter-user distance among the transmit-receiver user pair.
  FD-HetNet:
    Similar to FD-OFDMA, the power control can be performed for the FD BS and femtocell access points (FAPs) and HD users in FD-HetNet to optimize the network performance.
    However, both the inter-cell interference and RSI need to be considered jointly in optimizing the overall network performance.

## Slide 51: Resource Allocation Problem Summary (3)
Transmit Beamforming:
  The robust transmit beamforming algorithms can improve the signal strength at the receiver side,
  and meanwhile reduce the self interference subject to various design criteria.
    FD-MIMO: the transmit antenna set at each FD nodes can perform beamforming to simultaneously transmit information and reduce the interference to its own received signals
    FD-OFDMA:
      The FD BS is equipped with multiple antennas, consisting of transmit and receive antenna sets,
      while the users only operate in the HD transmission mode due to hardware constraint.
      The BS can construct beamformer to support multiple users in the downlink while maximizing the received SNRs at
      BS by minimizing the RSI.

## Slide 52: Resource Allocation Problem Summary (4)
Link Selection
  For a FD communication system, each antenna can be configured to transmit or receive the signals.
  This will create multiple possible virtual links between two nodes, with one virtual link representing the channel from a transmit antenna of one node to a receive antenna of the other.
  An important question arisen is how to optimally select the link for each direction to optimize the system performance.
    Antenna selection in FD-MIMO systems
    Joint antenna and relay selection in FD-Relay systems
    Coordinated multiple point transmission

## Slide 53: Resource Allocation Problem Summary (5)
Subcarrier Allocation
  In a FD-OFDMA network consisting of one FD BS with Nf subcarriers, Nu uplink users, and Nd downlink users,
    a fundamental challenge is how to pair uplink and downlink users, and allocate subcarrier across these user pairs;
    The subcarrier allocation involves
      allocating the different subsets of subcarriers to different users
      taking into account the RSI at the BS and the co-channel interference between the uplink and downlink users within each user pair.
  In FD-Relay networks, consisting of multiple source and destination nodes, and FD relay nodes using OFDM transmission,
    the corresponding subcarriers should be also properly allocated at the relay for different source-destination pairs.

## Slide 54: Conclusions
This tutorial presented the recent development of FD bascis and discussed representative FD communications:
  FD CRN, FD CSMA/CD, and FD-HetNet networks.
The associated resource allocation problems are discussed:
  e.g. mode switch, power control, link selection and pairing, interference-aware beamforming, and subcarrier assignment.
A few examples on FD resource allocation are illustrated:
FD communication is very promising, which enables many potential future research applications, e.g.,
  FD MIMO
  FD Relay networks
  FD Two Way Relay
  FD D2D
  FD OFDM