## Slide 1
Resource Allocation for Full-Duplex Communication and Networks
Zhu Han
Department of Electrical and Computer Engineering
University of Houston, Houston, TX, USA
Keynote, First International Workshop on Full Duplex Wireless Communications, Globecom Workshop, Washington D.C. 2016
Slides are available at :
http:wireless.eng.uh.edu/research.htm

## Slide 2: Table of Content
Basic of Full-duplex Communications
Full Duplex Crosslayer Design
  Full Duplex Cognitive Radio: Listen and Talk
  Full Duplex RF CSMA/CD
  Full Duplex HetNet
  Resource Allocation Summary
Conclusions
Overview of research lab

## Slide 3: KPIs 6 Key Performance Indicators (KPIs) for 5G
Chart: 
| 2010.0 | 2011.0 | 2012.0 | 2020.0
系列 1 | 1 | 2 | 4 | 20
1000X Capacity
(Traffic and Connections)
10Gbps
10X Peak Data Rate
(10+Gbps)
10X User Rate Anywhere
(100M-1Gbps)
1000X Energy&Cost Reduce
10X Low Latency,
High reliability
But what is 5G? D2D, small cell, Massive MIMO or full duplex?
5-10X Spectrum Efficiency

## Slide 4: Background of Full-Duplex Techniques
Traditional half duplex: using orthogonal resources
  Time-division duplex
  Frequency-division duplex
Problems
  Orthogonal resources are allocated for reception and transmission.
Solutions
  Same resources are allocated for reception and transmission
Time-division duplex
Frequency-division duplex
Spectral loss
Full-duplex
Comms

## Slide 5: Full Duplex Introduction
Allows communication at the same time and frequency resources.
Advantages
  High spectral efficiency
    Same time & same frequency band
  Low cost
    Readily use the existing MIMO radios
    Hardware advancement, etc.
: Signal of interest
: Self interference
Full duplex communication

## Slide 6: Main Challenges
Traditional Challenges
  Very large self interference
    50-110dB larger than signal of interest
    Depending on inter-node distance
  ADC is the bottleneck
    Limited dynamic range: saturation distortion.
    Limited precision: signal of interest is less than noise.
      1 bit ADC is 6 dB in SNR
      Self interference costs 8-18 bits
Need to reduce interference before ADC
Fig. 6 Very large Self interference
Self interference
Received signal
Signal of interest
Fig. 7 Signal after quantization

## Slide 7: Self-interference Cancellation
Self interference channel
Passive antenna propagation suppression
Active cancelation
  Active analog cancelation
  Active digital cancelation
Pre-mixer Post-mixer

## Slide 8: Passive Propagation Cancellation
MIMO system
  Example, two transmitting antenna has 180 degree difference at the receiving antenna
  Multiple antenna for beamforming, nulling and self-interference cancellation.
  Challenges: For wideband, wavelength
  is different, so the cancellation is not good

## Slide 9: Active Analog Cancelation (2)
Post-mixer
Post-mixer
Post-mixer
Pre-mixer
ADC
DAC
x
x
Post-mixer

## Slide 10: Active Digital Cancelation
Similar to equalizer
Two-step cancellation:
  Estimate the self residual interference channel hRI through training symbols
  Cancel hRIx[n] at baseband
Useless if interference is too strong (ADC bottleneck)

## Slide 11: Some existing prototypes
Stanford
Rice
Finland Aalto University
Beijing University

## Slide 12: Table of Content
Basic of Full-duplex Communications
Full Duplex Crosslayer Design
  Full Duplex Cognitive Radio: Listen and Talk
  Full Duplex RF CSMA/CD
  Full Duplex HetNet
  Resource Allocation Summary
Conclusions

## Slide 13: Listen-and-Talk Protocol For Cognitive Radio
Conventional Listen before talk
“listen-and-talk” (LAT) protocol
  simultaneously sense and access the vacant spectrum.
Yun Liao, Tianyu Wang, Lingyang Song, and Zhu Han, “Listen-and-Talk: Full-duplex Cognitive Radio Networks,” in Proc. IEEE Globecom’14, Austin, TX, Dec. 2014. Best Paper Award
Yun Liao, Lingyang Song, Yonghui Li, and Zhu Han, “Full-Duplex Cognitive Radio: A New Design Paradigm for Enhancing Spectrum Usage,” to appear, IEEE Communications Magazine [arxiv: http://arxiv.org/abs/1503.03954]

## Slide 14: The Listen Before Talk (LBT) Protocol
SUs sense the spectrum before transmission
  Sensing and transmission separate in time domain
Discontinuous transmission
Discontinuous sensing

## Slide 15: Motivation of Listen and Talk (LAT) Protocol
Discontinuous transmission
  Can never fully utilize spectrum holes for transmission
Discontinuous sensing
  Inevitable collision and spectrum waste
Continuous
Continuous
Detect PU’s state change in no time

## Slide 16: System Model
One PU
  Non-slotted
One FD-SU pair
  Each with two antennas
  SU1: secondary transmitter
  SU2: secondary receiver
  Slotted

## Slide 17: Listen-and-Talk Protocol (1)
Ant1 of SU1 senses the spectrum
Ant2 transmits if a spectrum hole is detected simultaneously

## Slide 18: Listen-and-Talk Protocol (2)
Four states of the system:
  1: only the PU uses the spectrum
  2: only SUs use the spectrum
  3: neither the PU nor SUs use the spectrum – spectrum waste
    3-A: change of PU’s state – PU leaves in a slot
    3-B: sensing error – false alarm
  4: both the PU and SUs use the spectrum – collision
    4-A: change of PU’s state – PU arrives in a slot
    4-B: sensing error – miss detection

## Slide 19: Sensing Threshold (1)
Received signal varies in association with SU1’s activity.
  Active SU1
  Silent SU1
Thus, the varies sensing thresholds are needed according to SU1’s state to achieve better sensing performance.
RSI

## Slide 20: Sensing Threshold (2)
How to set ε0 and ε1?

## Slide 21: Sensing Threshold (3)

## Slide 22: Sensing Threshold (4): Sensing Error
Sensing error includes two parts:
false alarm and miss detection

## Slide 23: Sensing Threshold (5): State Transition
State Transition: a discrete-time Markov chain
Notes: consider the steady-state distribution of the Markov chain

## Slide 24: Sensing Threshold (6): Collision Ratio
The sensing thresholds are determined by
  Constraint of the maximum collision ratio

## Slide 25: Power-Throughput Tradeoff (1): SU Throughput
The secondary throughput is
  R is the rate of transmission
  Pw is the time ratio of spectrum waste

## Slide 26: Power-Throughput Tradeoff (2)
Increase with RSI
Tradeoff between secondary transmit power and throughput
Optimal transmit power can be derived.

## Slide 27: Adaptive Switching
Comparison of the spectrum usage
Adaptive switching of the two protocol
Lower spectrum waste ratio
under strict constraint
Full utilization of spectrum holes
Spatial correlation factor
Sensing duration / Slot length

## Slide 28: Table of Content
Basic of Full-duplex Communications
Full Duplex Crosslayer Design
  Full Duplex Cognitive Radio: Listen and Talk
  Full Duplex RF CSMA/CD
  Full Duplex HetNet
  Resource Allocation Summary
Conclusions

## Slide 29: Full Duplex CSMA/CD
Liao Yun, Tianyu Wang, Kaigui Bian, Lingyang Song and Zhu Han, “Decentralized Dynamic Spectrum Access in Full-Duplex Cognitive Radio Networks,” IEEE International Conference on Communications (ICC), Best paper award, London, 2015.
Yun Liao, Kaigui Bain, Lingyang Song,and Zhu Han, “Full-duplex MAC Protocol Design and Analysis," appear, IEEE Communications Letters
Yun Liao, Kaigui Bian, Lingyang Song and Zhu Han, “Full-duplex WiFi: Achieving Simultaneous Sensing and Transmission for Future Wireless Networks,” ACM Mobihoc (poster), Hangzhou, China, 2015.
Roundabout example for CSMA, CSMA/CD and Aloha
RF half duplex can only use CSMA
Full duplex enable CSMA/CD
Performance gain when traffic is high

## Slide 30: Full Duplex Radom Access MAC in CRNs
With FD techniques, SUs can keep sensing during transmission.
Contention window: determine the optimal backoff length.
Handling the RSI: the RSI results in false alarm and miss detection

## Slide 31: Table of Content
Basic of Full-duplex Communications
Full Duplex Crosslayer Design
  Full Duplex Cognitive Radio: Listen and Talk
  Full Duplex RF CSMA/CD
  Full Duplex HetNet
  Resource Allocation Summary
Conclusions

## Slide 32: FD HetNet System Model
Single cell FDD OFDMA
Two-tier network
  base station (BS) and femto cell access point (FAP)
MIMO is equipped in BS and FAP.
Option to either connect to BS or one of SAPs

## Slide 33: Resource Allocation for FD HetNet
Compared with resource allocation in HD-HetNet
  Mode selection and connection selection
  Other resources such as power and channels
Notes: Since any node can operate either in FD or HD, and since frequency reuse is allowed on each subcarrier for one time, then each transmission on node (k) for user pair (n,m) on subcarrier (s) will have an interference transmission from node (k’) for transceiver pair (n’,m’).
Therefore, the throughput can be calculated by either case of the following cases.
  Both concerned node (k) and interference node (k’) operate in FD.
  The concerned node operates in FD and the interfering node operates in HD MU-MIMO.
  The concerned node operates in HD MU-MIMO and the interfering node operates in FD.
  Both nodes operate in HD MU-MIMO
 The details of each case will be illustrated in the upcoming slides.

## Slide 34: Numerical Results and intuition
Bias: connection to FAP and BS
Backhaul constraint
Switch between HD and FD
Notes: It is expected that by increasing the spatial correlation coefficients between antennas that the HD performance will degrade.
However, FD performance is independent of the spatial correlation between the antennas.
It can be clearly noticed that the proposed scheme was able to switch between FD and HD to choose the transmission mode with the highest throughput

## Slide 35: Resource Allocation Problem Summary
Adaptive Mode Switch
  Half-duplex radio
  Full-duplex radio
Power Control
  High power will introduce self interference
  Mode selection and power control are coupled
Transmit Beamforming
  How many antenna for self interference cancellation
OFDM, Subcarrier Allocation
Link Selection
Routing

## Slide 36: Conclusions
Full Duplex Basics
  Key is self interference before ADC
Good thing: whole resource allocation can be redo
  FD MIMO
  FD Relay networks
  FD Two Way Relay
  FD D2D
  FD OFDM
  …
Bad thing: full duplex is
not always better than
half duplex
Human being is full duplex
Brain cancel self interference

## Slide 37: Useful info for Research on FD Comms
Full-duplex communication website
  http://wireless.pku.edu.cn/home/songly/fullduplex.html
    Tutorial and survey, books, technical papers, standardization…
Books
  Yun Liao, Tianyu Wang, Lingyang Song, and Zhu Han, “Listen-and-Talk: Full-Duplex Cognitive Radio,” with Springer, 2016.
  Lingyang Song, Risto Wichman, Yonghui Li, and Zhu Han, “Full-Duplex Communications and Networks,” print, Cambridge University Press, UK.
  Tutorials
  Lingyang Song and Zhu Han, “Resource Allocation for Full-Duplex Wireless Communication and Networks,” IEEE International Conference on Communications (ICC), London, UK, Jun. 2015
  Lingyang Song and Zhu Han, “Full-Duplex Wireless Communication and Networks: Key Technologies and Applications,” IEEE International Conference on Communications in China (ICCC 2014), Shanghai, China, Oct. 2014