## Slide 1: Satellite Communication System
Yan Zhu
09/21/2019

## Slide 2: Outline
Introduction
Orbits and Related Issues
Frequency Band Selection
System Composition
Satellite Channel
Conclusion

## Slide 3: Introduction
What is the satellite communications?
Satellite communication is the communication between two or more earth stations (user terminals) by using artificial earth satellites as relay stations to forward radio waves.
Satellite communication has three forms:
Between satellite and earth station;
Between satellites;
Between earth stations via satellites.

## Slide 4: Features
Launch and control technology is complex
Propagation delay is large
Affected by outer space
Communication distance is long
Service scope is wide
Communication quality is good
Not restricted by geographical conditions
Wide available bandwidth
Large communication capacity
Independent of the ground communication
Network routing is simple.
Network construction is fast and low cost.
Secure communication.
Communication costs are independent of communication distance.

## Slide 5: Development
The idea of satellite communications was first proposed by British Air Force officer Arthur C. Clarke (science fiction writer) in the “Wireless World" magazine "Extra-Terrestrial Relays" (1945).

## Slide 6: Development
The former Soviet Union launched the world's first artificial earth satellite, Sputnik I.
The US launched the "Skool" broadcast test satellite for the transmission of tape recording signals.
The US launched the "Echo" (ECHO) satellite, the first completed active delay relay communication.
“TELESTAR-1” LEO satellite laid the technical foundation for commercial satellite communications.
The US radio company RCA launched the "Relay-1“.
Syncom 3: first truly geosynchronous orbit satellite.
1957.10
1964.8
1962.11
1962.7
1960.8
1958.12

## Slide 7: Development
International Telecommunications Satellite Organization launched the “International Communication Satellite” I in April 1965, which is the world’s first practical geosynchronous orbit communication satellite and marks the beginning of the practical phase of satellite communications.
For more than 50 years, satellite communications have developed rapidly:
Satellite weights: tens of kilograms -> more than 5,000 kilograms.
Life spans: 1.5 years -> more than 15 years.
Communication capacity: 480 tones -> tens of thousands of tones.
Traffic: TV, data, multimedia services.

## Slide 8: v.s. Cell
More than 80% of the land and more than 95% of the sea area in the world lack effective broadband information coverage.
Problems of terrestrial networks:
Cells: constantly split, base station configuration problem
Expensive infrastructure investment in low population density areas
Limited communication in the air, ocean and special occasions
multi-hop network, high complexity, service quality cannot be guaranteed
Advantages of satellite communications
Battlefield individual personal communication system
Civil personal communication field
Wireless broadband multimedia applications
Global seamless coverage, etc.

## Slide 9: Outline
Introduction
Orbits and Related Issues
Frequency Band Selection
System Composition
Satellite Channel
Conclusion

## Slide 10: Orbits
Height:
Low orbit < 5,000km, operation period: 2~4 hours
Medium orbit: 5,000~20,000km, operation period: 4~12 hours
High orbit > 20,000km, operation period:12~ 24 hours
Shape:
Circular
elliptical orbit
Angle:
Equatorial orbit: 0°
Polar orbit: 90°
Inclined: 0° to 90°

## Slide 11: Orbits
GEO (geostationary earth orbit)
Height: 36,000 km
Orbital period: 24 hours.
Propagation delay: 250ms.
The coverage area is stable.
LEO (low earth orbit)
Height: 500~1,500km
Orbital period: 1.5~2 hours
Propagation delay: < 10ms
Doppler effect
Maximum visible time: 20 minutes.
Signal propagation distance: short
Link loss: small
Transmission power: low
MEO (medium earth orbit)
Height: 8000km~18000km
Orbital period: 5-10 hours
Propagation delay: 50ms.
Maximum visible time: a few hours.

## Slide 12: Orbits
Advantages of GEO satellites:
Fixed to the Earth, Convenient to point to the satellite
Doppler shift is negligible.
Satellite tracking is simple.
Large coverage area.
Problems of GEO satellite:
Signal attenuation is large.
Launch and control technology of GEO satellites: complex.
Polar regions -> blind spots, and high latitudes communications are not good.
Eclipses and daily interruptions.
Large signal transmission delay and echo interference.
Hence, the future satellite orbit selection is turning to choose the LEO and correspondingly increase the number of satellites to deal with the problem of the coverage.

## Slide 13: Orbits
Track height selection
Van Allen belt: A harsh electric radiation environment, strong electromagnetic radiation. α particles, protons and high energy particles are destructive to the circuit.
Inner layer: 1,500-5,000 km
Outer layer: 13,000-20,000 km
Atmospheric resistance on satellite motion: altitude < 700 km.
Three suitable windows: 700~1,500km; 5,000~Near 13,000km; more than 20,000 km.
Factors to select the track
Height: Higher the satellite -> Larger the coverage area -> Greater the fading
Elevation angle: Angle between the earth station antenna and the ground plane: 0 ~ 70 degree.
Propagation time: Propagation distance / speed of light.
Interference: Same and adjacent channel interference.
Launch vehicle performance: Rocket technology and reliability.

## Slide 14: Outline
Introduction
Orbits and Related Issues
Frequency Band Selection
System Composition
Satellite Channel
Conclusion

## Slide 15: Frequency
Satellite communication band (microwave)
Frequency | Range(GHz) | Frequency | Range(GHz)
UHF | 0.3~1.12 | Ku | 12.4~18
L | 1.12~2.6 | K | 18~26.5
S | 2.6~3.95 | Ka | 26.5~40
C | 3.95~8.2 | Millimeter wave | 40~300
X | 8.2~12.4 |  | 
Frequency allocation
The ITU divides the world into three regions:
Region 1: Europe, Africa, the Middle East and some countries of the former Soviet Union;
Region 2: America;
Region 3: In addition to the Asian region of the Middle East and some countries of the former Soviet Union and Oceania

## Slide 16: Frequency
Satellite communication:
Higher frequencies -> Higher information rates
Loss of electromagnetic waves related to frequency
Rain and fog
Scatter and absorb high frequency waves, causing greater losses, called rain attenuation
Higher frequency -> more severe rain attenuation.
Atmospheric absorption and rain attenuation
Frequency < 10 GHz, the loss is small and flat
Frequency > 12 GHz, the loss rises rapidly
Frequency > 60 GHz, unsuitable for satellite transmission
Atmosphere attenuation

## Slide 17: Frequency
Main factors of selecting a working frequency band:
External interference noise received by the antenna system -> small
Wave propagation loss -> small
Equipment applicable to this frequency band -> light in weight and small in size
Available frequency bandwidth -> meet the requirements for transmitting information
Mutual interference with other terrestrial wireless systems -> as small as possible
Make use of existing communication technologies and equipment as much as possible.

## Slide 18: Outline
Introduction
Orbits and Related Issues
Frequency Band Selection
System Composition
Satellite Channel
Conclusion

## Slide 19: System
System composition
Space segment: including satellite and measurement and control;
Ground segment: earth station

## Slide 20: Space Segment
Space segment
Satellites (platform and payload),
Satellite Control Center (SCC),
Tracking Telemetry and Command Station (TT&C).
Several concepts of space segments
Uplink: Radio waves from the ground segment to the satellite.
Downlink: Radio waves from the satellite to the ground segment.
Link quality: determining the bit error rate (BER)
Multiple access technology: FDMA, TDMA, CDMA, SDMA
Interstellar link: Communication link between satellites
Payload and platform: Power supply, structure, solar panels, etc.
Satellite role: amplify carrier, frequency conversion.
Repeater: transparent and regenerative repeater.
Satellite redundancy, lifetime, reliability

## Slide 21: Ground Segment
Ground segment: In a narrow sense: the ground segment is the earth station.
Several concepts of the ground segment
Earth station classification: large station, small station / single receiving, and receiving
Earth station structure: antenna, duplexer, power supply, tracking, monitoring, etc.
Signal processing technology: multiplexing, encryption, voice interpolation, compression, etc.

## Slide 22: Outline
Introduction
Orbits and Related Issues
Frequency Band Selection
System Composition
Satellite Channel
Conclusion

## Slide 23: Channel
Outside the ionosphere -> free space propagation
Propagation in the atmosphere can be corrected on free space propagation.
Except satellite mobile channel, the satellite channel between the satellite and earth station can be considered as a constant channel.
The radio waves are subject to loss in propagation atmosphere, rain, clouds, snow, fog, etc.
Satellite mobile communications (between NGEO satellite and mobile users) use lower communication frequencies and (semi) omnidirectional antennas, so as with ground mobile communications, there are multipath and shadow occlusions, which are fading channels.
Because the fixed earth station uses a directional antenna, the operating frequency is high, and the occlusion can be avoided, the satellite channel between the earth station and satellite can be regarded as a Gaussian white noise channel at this time.

## Slide 24: Channel (Inter-Satellite Link)
Inter-Satellite Link (free space loss)
Receiving power:
Effective area of an antenna:
Expression for the received power:
Fig. The power received by a receiving antenna.
Transmit power
Transmit antenna gain
Effective aperture area
Distance R
Where free space loss
Receiving gain
Wave length

## Slide 25: Channel (Inter-Satellite Link)
The origins of noise are as follows:
Natural sources
Noise in the receiving equipment.
Carriers from unwished transmitters
Fig. Spectral density of white noise.
Real noise sources do not always have a constant power spectral density, but the model is convenient for representation of actual noise observed over a limited bandwidth.
Power spectral density (W/Hz)
Equivalent noise power N (W)
Equivalent noise bandwidth
Noise characterization

## Slide 26: Channel (Inter-Satellite Link)
Carrier power to noise power spectral density ratio at receiver input
Fig. The geometry of an uplink.
Fig. The geometry of a downlink.
Effective Isotropic Radiated Power (EIRP)
Path loss L
Noise temperature T=, k is the Boltzmann constant
=(transmitter EIRP)(1/path loss)x(composite receiving gain/noise temperature)x(1/k) Hz

## Slide 27: Channel (Inter-Satellite Link)
Satellite-Ground Link (free space loss + attenuation in the atmosphere)
Fig. Losses in the terminal equipment.
The attenuation of waves in the atmosphere, denoted by
The overall effect on the power of the received carrier can replace by the path loss, L:
Carrier power to noise power spectral density ratio at receiver input

## Slide 28: Channel (mobile channel)
General physical channel model
Line of sight (LOS) signal >> the others (different from ground networks).
The wireless channel (LEO satellites, relay satellite and ground stations): Rician fading channel model with AGWN.
The signal received at destination at the time slot t is
J. Du, C. Jiang, J. Wang, Y. Ren, S. Yu, and Z. Han, “Resource allocation in space multiaccess systems,” IEEE Trans. Aerosp. Electron. Syst., vol. 53, no. 2, pp. 598–618, Jul. 2017.
: data transmitted
G: transmitting power
distance between i and j
Γ: path loss exponent
: additive Gaussian noise at t with zero mean and variance
channel fading coefficient modeled as a circularly symmetric complex Gaussian random variable where and are modeled as Gaussian random variable.

## Slide 29: Channel (mobile channel)
Distribution of: Rician probability density function (PDF)
signal-to-noise ratio (SNR) between two nodes i and j , specified as
Where follows the noncentral chi-squares () distribution with the PDF as
: power due to the LOS signal
: zeroth order modified Bessel function
total power of the LOS and scattering signal
: ratio between the power in the direct path and the power in the other scattered paths

## Slide 30: Channel (mobile channel)
Outage probability: failure of the packet transmission and reception.
Outage: SNR < given threshold .
Outage event can be expressed as the following equation:
Then, the success probability of the packet between i and j at SNR threshold is
where denotes the success transmission between nodes i and j .

## Slide 31: Channel (mobile channel)
Doppler effect
Fast moving satellites: frequency shift of dozens of kilohertz relative to a ground station.
Magnitude of Doppler effect: changes due to earth curvature
Fig. Geometry for Doppler effects
26820 km/h (H: 800 km)
13993 km/h (H: 18000 km)
Doppler frequency in the forward link:
Received carrier frequency at the satellite is
fractional Doppler of feeder link
transmitted carrier frequency from the satellite access node for the i-th user terminal inside the n-th spot beam
Q. Liu, "Doppler measurement and compensation in mobile satellite communications systems," in Proc IEEE MILCOM, Atlantic City, NJ, 1999

## Slide 32: Channel (mobile channel)
Transmitted carrier frequency by satellite for the mobile link
fractional satellite translation error
satellite translation
frequency.
Received carrier frequency by user terminal
total frequency error caused by both Doppler and satellite translation error

## Slide 33: Channel (mobile channel)
Total frequency error
forward feeder link Doppler
satellite translation error
forward mobile link Doppler
Doppler frequency in the return link:
The received carrier frequency by the satellite
transmitted carrier frequency by the i-th user terminal in the n-th spot beam.
fractional Doppler of the mobile link for
the i-th user in the n-th spot beam.

## Slide 34: Channel (mobile channel)
Transmitted carrier frequency by the satellite
Received carrier frequency by the radio frequency terminal
satellite translation frequency from the mobile link to the feeder link.
Total frequency error for the return link
The random Doppler frequency errors of very large range in the forward link and the return link must be compensated to achieve carrier frequency synchronization,

## Slide 35: Channel (mobile channel)
Doppler Compensation
The goal of the Doppler compensation for each control channel is to make sure that the received carrier frequency on the median Doppler line is the preassigned nominal frequency.
Carrier frequency that should be transmitted by the radio frequency terminal
Total frequency correction at the satellite access node
Nominal frequency for the n-th spot beam
Total frequency correction at the satellite access node

## Slide 36: Channel (mobile channel)
Fractional Doppler of the feeder link and Fractional satellite translation error can be measured by two pilot loops in the feeder link operated by the radio frequency terminal
Derived instantaneous fractional Doppler in the feeder link
Derived fractional satellite translation error
Transmitted frequency of the radio frequency terminal
satellite translation frequency

## Slide 37: Channel (rain attenuation)
Rain attenuation channel
D. Zhou, M. Sheng, R. Liu, Y. Wang and J. Li, "Channel-Aware Mission Scheduling in Broadband Data Relay Satellite Networks," in IEEE Journal on Selected Areas in Communications, vol. 36, no. 5, pp. 1052-1064, May 2018.
SNR of a downlink in slot t can be expressed as follows
is the transmission power (in W) of a relay satellite to one of its ground station in slot t.
The relay satellite transmitting antenna gain in slot t is presented as
maximum antenna gain.
: off-axis angle with respect to maximum radiation
: half power angle of transmitting antenna.
is expressed as

## Slide 38: Channel (rain attenuation)
Rain attenuation mainly influenced by frequency, elevation angle, altitude above sea level.
Rainfall intensity can be expressed as:
For the GEO satellite, can be denoted as
Here, and are the effective radius of the Earth (6400 km) and the elevation angle, respectively.
(dB/km): attenuation per kilometer in slot t.
(in km): equivalent effective slant-path length.

## Slide 39: Channel (rain attenuation)
Given the difference of longitude between a ground station and relay satellite α and the latitude of the ground station , can be calculated as
: height above mean sea level of the ground station (ITU-R P.839).
Besides, rain height can be expressed as

## Slide 40: Channel (rain attenuation)
According to Recommendation ITU-R P.838, attenuation per kilometer can be calculated according to the following equation
Where, R (mm/h) is rainfall intensity. Coefficients ρ and η are function of frequency f in 1 ∼ 1000 GHz (ITU-R P.838).

## Slide 41: Channel Reference
Reference
[1] Chun Loo, "A statistical model for a land mobile satellite link," in IEEE Transactions on Vehicular Technology, vol. 34, no. 3, pp. 122-127, Aug. 1985.
[2] C. Loo, "Digital transmission through a land mobile satellite channel," in IEEE Transactions on Communications, vol. 38, no. 5, pp. 693-697, May 1990.
[3] B. Vucetic and J. Du, "Channel modeling and simulation in satellite mobile communication systems," in IEEE Journal on Selected Areas in Communications, vol. 10, no. 8, pp. 1209-1218, Oct. 1992.
[4] G. E. Corazza and F. Vatalaro, "A statistical model for land mobile satellite channels and its application to nongeostationary orbit systems," in IEEE Transactions on Vehicular Technology, vol. 43, no. 3, pp. 738-742, Aug. 1994.
[5] Yongjun Xie and Yuguang Fang, "A general statistical channel model for mobile satellite systems," in IEEE Transactions on Vehicular Technology, vol. 49, no. 3, pp. 744-752, May 2000.
[6] Wenzhen Li, Choi Look Law, V. K. Dubey and J. T. Ong, "Ka-band land mobile satellite channel model incorporating weather effects," in IEEE Communications Letters, vol. 5, no. 5, pp. 194-196, May 2001.
[7] J. Du, C. Jiang, J. Wang, Y. Ren, S. Yu, and Z. Han, “Resource allocation in space multiaccess systems,” IEEE Trans. Aerosp. Electron. Syst., vol. 53, no. 2, pp. 598–618, Jul. 2017.
[8] D. Zhou, M. Sheng, R. Liu, Y. Wang and J. Li, "Channel-Aware Mission Scheduling in Broadband Data Relay Satellite Networks," in IEEE Journal on Selected Areas in Communications, vol. 36, no. 5, pp. 1052-1064, May 2018.

## Slide 42: Conclusion
Satellite network | Differences | Terrestrial network
Through Earth-orbiting satellites | Data transmission | Through land-based cell towers
Fewer gaps | Coverage | More potential for gaps
Usually available in any location | Use in remote locations | Can be difficult, even impossible
More expensive than cellular | Affordability | Less expensive than satellite
May experience delays due to long-distance data transfer or changes in weather | Reliability | May experience interruptions as machine moves through network
Less vulnerable | Disaster risk | More vulnerable

## Slide 43: Conclusion
Satellite communications have many advantages especially in the aspects of the global coverage and long-distance communications.
However, the large propagation delay and the path loss are still the long-range problems of the satellite communications.
Future satellite communications are turning to miniaturization, functionalization. In virtue of the advantage of the LEO satellites, large-scale satellite networking and routing algorithm will undoubtedly increase the network capacity and decrease the network latency.
With the introduction of modern technologies, such as SDN/NFV, smart antenna, massive MIMO, beamforming, satellite communications must be the one of the most important component in the future generation of wireless communications.

## Slide 44: Reference
Reference books
[1] J. Pelton, S. Madry, and S. Lara, Handbook of satellite applications, Springer, 2012.
[2] L. Lppolito, Satellite communications systems engineering, Wiley, 2017.
[3] G. Maral and M. Bousquet, Satellite communications system, Wiley, 2009.
[4] S. Ohmori, H. Wakana, and Seilchiro Kawase, Mobile satellite communications, Artech House, 1997.
[5] M. Rich haria, Mobile satellite communications: principles and trends, John Wiley & Sons, 2014.

## Slide 45: THANK YOU