## Slide 1
Dynamic Control Algorithm Design
Based on Lyapunov Stability Theory
Zhu Han
Thanks for Zirui Zhuang and Ruoguang Li

## Slide 2
Outline
5
Conclusions
2
Lyapunov Optimization
- Lyapunov
- Lyapunov stability
- Asymptotically stability
- Second Method of Lyapunov
- Discrete form in time-slotted systems
1
Lyapunov and Stability Theory
4
Lyapunov-Based Reinforcement Learning for Network Routing
3
Dynamic Cache Placement, Node Association, and Power Allocation

## Slide 3
Aleksandr Mikhailovich Lyapunov, 1857-1918
  a mathematician, mechanician and physicist
Known for his contribution to the analysis of the stability of nonlinear dynamical systems
Lyapunov and Stability Theory
Original work done by Lyapunov in 1890s
Improved by N. G. Chetaev in 1930s
Skyrocketed in aerospace guidance systems in 1960s
Notes: The original work is done by Lyapunov as his thesis “The General Problem of Stability of Motion”, 1892, in Russian.
Nikolay Gur'yevich Chetaev continued the work from 1930s to 1940s, all published in Russian. Some of his work were translated into English in 1961.
In 1960s, the so-called "Second Method of Lyapunov" (see the following pages) was found to be applicable to the stability of aerospace guidance systems which typically contain strong nonlinearities not treatable by other methods.

## Slide 4
  System state
  System function
Lyapunov and Stability Theory
System Stability in the Sense of Lyapunov
System state starts “close enough” to the equilibrium
remains “close enough” forever

## Slide 5
Lyapunov and Stability Theory
Asymptotical Stability
System state starts “close enough” to the equilibrium
remains “close enough” forever,
eventually converges to the equilibrium
  System state
  System function

## Slide 6
Lyapunov and Stability Theory
Another example

## Slide 7
  Lyapunov stability
  asymptotic stability
Lyapunov and Stability Theory
Second Method of Lyapunov
a.k.a. the Direct Method
Lyapunov function
There is no need of explicitly knowing the systems’ functions.
It is extremely suitable for non-linear complex networked systems.
Notes: The analog to energy in physical systems. The system’s state reaches the attractor when there is no more energy left.
And the Second Method of Lyapunov do not need the actual energy functions of physical systems.
For non-linear systems, the actual functions may be difficult to formulate. Yet a Lyapunov function may be easier to find, relatively.

## Slide 8
  Define distance function
  System Stability in the Sense of Lyapunov
  Asymptotical Stability
Lyapunov and Stability Theory
Discrete form in time-slotted systems

## Slide 9
Outline
5
Conclusions
2
Lyapunov Optimization
1
Lyapunov Stability
4
Lyapunov-Based Reinforcement Learning for Network Routing
- Static Networks with Fixed States
- Dynamic Networks
- Queue Model
- Queue Stability
- Lyapunov Optimization
- Details
- Performance-Backlog Tradeoff
- Application to Mobile Networks with Unreliable Channels
3
Dynamic Cache Placement, Node Association, and Power Allocation

## Slide 10
Static Networks with Fixed States
General One-Shot Optimization Framework
s.t.
…
This optimization framework generally does not consider the system-level features (e.g., stability of the system).
Lyapunov Optimization

## Slide 11
Dynamic Networks
Random events, time variation, and uncertainty
  Wireless mesh networks with opportunistic scheduling
  Ad-hoc mobile networks with peer-to-peer communications
  Smart grid architecture with energy distribution
  ……
Focuses on queueing system
Time-average optimization subject to time-average constraints and queue stability
other constraints within current time slot
queue stability
Lyapunov Optimization

## Slide 12
Queue Model [1]
Queue Dynamics (Backlog): A single-server discrete-time queueing system
Fig.1 Queue Model
[1] M. J. Neely, “Stochastic network optimization with application to communication and queueing systems,” in Synthesis Lectures on Com- munication Networks. San Rafael, CA, USA: Morgan & Claypool, 2010, vol. 3, pp. 1211, 1
  and are assumed to be non-negative
  is generally a Poisson process
  is assumed to be a non-negative real valued random variable for all slots t
Lyapunov Optimization

## Slide 13
Queue Stability
Strongly Stable: A queue is strongly stable if
Rate Stable: A queue is rate stable if
with probability 1
Mean Rate Stable: A queue is mean rate stable if
Considers the time average expected backlog
Lyapunov Optimization

## Slide 14
Lyapunov Optimization
Sender
Receiver
Find the tradeoff between objective optimization and queue stability
Two goals
  Make sure the queue to remain strongly stable
  Minimize the penalty/cost or maximize the reward
Tradeoff
  More departure in queue (good for queue stability) →larger departure rate→larger cost (i.e. more power consumption)
  →increased penalty
  Decrease penalty →smaller cost (less power consumption) →less departure in queue (bad for queue stability)
Fig.2 Design algorithm to control the backlog
Lyapunov Optimization

## Slide 15
Lyapunov Function:
Lyapunov Drift:
Details
Tackle the time average constraint : introducing the virtual queues
Lyapunov Function:
“Virtual” means does not represent a real data backlog
A way to turn the time average inequality constraint into a pure queue stability problem
Lyapunov Drift:
i.i.d.: One-time slot
Non i.i.d.: T-time slot
i.i.d.: One-time slot
Non i.i.d.: T-time slot
Lyapunov Optimization
Notes: The bound D and B are both related to the arrival rate a_i(t) and service rate b_i(t).
Z(T+1) >= Z(t) + g(t)

## Slide 16
Important Inequality (e.g. one time slot drift)
+
where we use the fact that
+++2
Finally, we have
B+
Lyapunov Optimization
Notes: B(t)=1/2*Sum{[a(t)-b(t)]^2}

## Slide 17
Connection Between Objective and Queue
Drift plus penalty (minus reward) function:
Optimize the drift plus penalty (minus reward) function:
V: 1. non-negative control parameter
2. larger V leads to more emphasis on penalty minimization
Obtain the control decision by minimizing the right-hand-side of the inequality at every time slot t
Lyapunov Optimization

## Slide 18
Performance-backlog Tradeoff
The time-average queue length yields:
Minimum penalty bound:
[O(V),O(1/V)] tradeoff
Tuning V to be sufficiently large so that the minimum penalty can be achieved (+)
Time average queue backlog bound increase linearly with V. (-)
+
Non i.i.d.
i.i.d.
Non i.i.d.
i.i.d.
Lyapunov Optimization
Notes: independent and identically distributed random event process

## Slide 19
Application to Mobile Networks with
Unreliable Channels
= Stationary Node
= Locally Mobile Node
= Fully Mobile Node
= Sink

## Slide 20
Application to Mobile Networks with
Unreliable Channels
Assumptions:
Random Arrivals i.i.d. over slots.
Rate vector (bits/slot)
2) Random Channel states i.i.d. over slots.
3) Transmission Rate Function
--- Power allocation during slot t
--- Channel state during slot t
t
0 1 2 3 …
Time slotted system ()
l1
l2
lN
rate mi
power P
Good
Med
Bad

## Slide 21
Application to Mobile Networks with
Unreliable Channels
Control: Allocate power () in reaction to current channel state and current queue backlogs.
Goal: Stabilize with Minimum Average Power while also maintaining Low Average Delay.
Avg. Power and Avg. Delay are Competing Objectives
maximize:
subject to:
t
0 1 2 3 …
Time slotted system ()
l1
l2
lN
rate mi
power P
Good
Med
Bad

## Slide 22
Application to Mobile Networks with
Unreliable Channels
Avg. Power
Avg. Delay
Performance-Delay Tradeoff: [O(1/V), O(V)]
Average Power Versus Delay
[Neely, Urgaonkar 2006, 2009]

## Slide 23
Outline
3
Dynamic Cache Placement, Node Association, and Power Allocation
5
Conclusions
2
Lyapunov Optimization
1
Lyapunov Stability
4
Lyapunov-Based Reinforcement Learning for Network Routing
- Contributions
- System Model
- Optimization Problem Formulation
- Lyapunov Optimization Framework
- Simulation Results

## Slide 24
Contributions [2]
Try to investigate the cache placement, node association, and resource allocation in the time slotted system.
Model the dynamic content popularity evolution.
Utilize Lyapunov optimization framework to connect utility maximization and queue stability.
Use greedy method and Generalized Benders decomposition to solve the proposed problem (online MINLP) at every time slot.
System Model
  Library of video files
  Edge Node (EN)
  Mobile user
  Slotted time t
  Assumptions
  Channel state information (CSI) changes every time slot.
  Node association is pre-scheduled.
  TDMA is implemented during transmission.
Fig.3 Edge Caching in Fog-aided wireless Networks
[2] Ruoguang Li, Li Wang, Yanmin Gong, Mei Song, Miao Pan, and Zhu Han," Dynamic cache placement, Node association, and power allocation in fog aided networks," accepted, 2019 Global Communications Conference (Globecom), Waikoloa, HI, USA.
Dynamic cache placement, node association, and power allocation

## Slide 25
Optimization Problem Formulation
Average power consumption constraint
Storage capacity constraint
Utility function
Caching decision
User-fog association decision
Dynamic cache placement, node association, and power allocation

## Slide 26
Lyapunov Optimization
Step 1: construct a virtual queue, to eliminate the time-average constraint
Step 2: define Lyapunov function
Step 3: define T-slot Lyapunov drift
Step 4: define drift-minus-reward
Dynamic cache placement, node association, and power allocation

## Slide 27
Lyapunov Optimization
We have the inequality
Solving the right-hand-side, we define the new objective function
Greedy + Generalized Benders decomposition
Dynamic cache placement, node association, and power allocation

## Slide 28
Simulation Results
Average queue length becomes stable over a period of time and oscillates around a certain value;
Larger V leads to lager utility, as well as larger average queue length.
Dynamic cache placement, node association, and power allocation

## Slide 29
Outline
5
Conclusions
2
Lyapunov Optimization
1
Lyapunov Stability
4
Lyapunov-Based Reinforcement Learning for Network Routing
- Challenges for Communication Networks Today
- State of the Art
- System Model
- Queuing Dynamics
- Lyapunov Drift
- Lyapunov-Based Reinforcement Learning
- Simulation Results
3
Dynamic Cache Placement, Node Association, and Power Allocation

## Slide 30
Multimedia streaming services generate large volume of delay-sensitive network traffic.
Emerging IoT services generate massive sensory and time-series data.
The network traffic burst as social event happens, exceeding the capacity on critical links.
The network operators face increasing cost on expanding the network’s capacity as we enters the Post-Moore Era.
Lyapunov-Based Reinforcement Learning for Network Routing
Challenges for communication networks today
We need to find out how to route the network traffic more optimally
Notes: The death of Michael Jackson brought down the Internet, which is ten years ago when smartphones has limited functionality and the user generated traffic is relatively low compared with what it is today.
As the cost becomes higher, network operators cannot just simply add capacity to critical links. Optimization is needed.

## Slide 31
Stochastic network optimization, usually based on the Lyapunov’s methods, can be used to enforcing the networked system’s stability.
  Yet these methods maximizing the system’s stability and minimizing the penalty in the sense of t-time-slot time-average.
Reinforcement learning based methods are used to provide adaptive network control, maximizing the system’s rewards (minimizing the penalty),
  yet without mathematically proven stability guarantees.
Lyapunov-Based Reinforcement Learning for Network Routing
State of the Art

## Slide 32
The arrival of network traffic can be modelled by a Markovian Arrival Process (MAP).
  MAP is sufficiently dense so it can be used to approximate any arbitrary stochastic point process. Not just limited to a Poisson process.
  MAP can represent the time-correlation in arrival network traffic.
The control policy decides the routing function, where its element denotes the bandwidth allocated on link from node to node for traffic destined to node .
Lyapunov-Based Reinforcement Learning for Network Routing
System Model

## Slide 33
Queuing dynamics
Lyapunov-Based Reinforcement Learning for Network Routing
Queuing Dynamics
Queue backlog size
Markovian arrival
Arrival by forwarding
Departure by forwarding

## Slide 34
Define Lyapunov function
Lyapunov Drift
Lyapunov-Based Reinforcement Learning for Network Routing
Lyapunov Drift

## Slide 35
Define Lyapunov function
Lyapunov Drift
  Prerequisite: the arrival of network traffic is within the system’s capacity region, which leads to
  If the queue backlog size is sufficiently large, say
  Then
Lyapunov-Based Reinforcement Learning for Network Routing
Lyapunov Drift
It is possible to design a control policy to make the queue backlog size stable

## Slide 36
Optimization objective
  Minimizing the Lyapunov Drift to achieve better stability
  Minimizing the end-to-end latency of network traffic
  Drift plus penalty
Deep Reinforcement Learning
Lyapunov-Based Reinforcement Learning for Network Routing
Lyapunov-Based Reinforcement Learning
Environment
State
Lyapunov Optimization
Action
Rewards

## Slide 37
Drift plus penalty
Deep Reinforcement Learning
  Rewards:
  Q value update:
  Action selection:
Lyapunov-Based Reinforcement Learning for Network Routing
Lyapunov-Based Reinforcement Learning

## Slide 38
Link bandwidth 100 Mbps
Imbalance propagation delay
The propagation delay will shift from -10% to 10% every 4 seconds.
The traffic is generated using an ON-OFF model with probability p.
The mean value of traffic volume is from a set of uniformly generated traffic matrix.
The transition between the states follows a fixed state transition matrix.
Experiment Setup
10 ms
10 ms
10 ms
10 ms
10 ms
10 ms
10 ms
10 ms
100 ms

## Slide 39
Lyapunov-Based Reinforcement Learning for Network Routing
Simulation Results
The proposed method achieves better stability compared with basic Lyapunov optimization method without reinforcement learning
The lower value of p is, the higher burstiness there will be in the system.
Notes: The upper figure shows the proposed methods is better than the original backpressure routing which uses basic Lyapunov optimization without reinforcement learning part.

## Slide 40
Lyapunov-Based Reinforcement Learning for Network Routing
Simulation Results
Also shows a tradeoff between queue stability and penalty minimization.
A larger V leads to smaller end-to-end latency, while the queue backlog size becomes larger as well.
Notes: The performance is saturated after V being greater than 10.

## Slide 41
Conclusions
Conclusions
  Content popularity evolves over time, how to design caching strategy under this scenario?
  New method to predict the content popularity, deep learning way, Monte Carlo Markov Chain…
  The true story behind Lyapunov optimization, the theoretical analyses of queue length bound, the choice of control parameter, etc.
  New solutions to handle the coupling of integer variables, e.g. McCormick envelope, big-M method, etc.
  Using Lyapunov-based reinforcement learning to solve problems where there are sophisticated pattern and time-correlation in the arrival process.

## Slide 42
Conclusions
References
J. Wu, Y. Zhou, D. M. Chiu and Z. Zhu, “Modeling Dynamics of Online Video Popularity,” IEEE Transactions on Multimedia , vol. 18, no. 9, pp. 1882-1895, Sept. 2016.
M. J. Neely, “Stochastic network optimization with application to communication and queueing systems,” in Synthesis Lectures on Communication Networks. San Rafael, CA, USA: Morgan & Claypool, 2010, vol. 3, pp. 1211, 1.
J. Ji, K. Zhu, R. Wang, B. Chen, and C. Dai, “Energy Efficient Caching in Backhaul-Aware Cellular Networks with Dynamic Content Popularity,” Wireless Communications and Mobile Computing, 2018.
X. Xu, J. Liu and X. Tao, "Mobile Edge Computing Enhanced Adaptive Bitrate Video Delivery With Joint Cache and Radio Resource Allocation," in IEEE Access, vol. 5, pp. 16406-16415, 2017.
Y. Guo, Q. Yang, J. Liu and K. S. Kwak, "Quality-Aware Streaming in Heterogeneous Wireless Networks," in IEEE Transactions on Wireless Communications, vol. 16, no. 12, pp. 8162-8174, Dec. 2017.

## Slide 43
Thank you!

## Slide 44
Case Study
Caching Model and Transmission Model
Transmission rate from EN i to user j
Transmission rate from EN i to user j
The probability of user requesting video [6]
[6] X. Xu, J. Liu and X. Tao, "Mobile Edge Computing Enhanced Adaptive Bitrate Video Delivery With Joint Cache and Radio Resource Allocation," in IEEE Access, vol. 5, pp. 16406-16415, 2017.

## Slide 45
Case Study
Queue Length of Service Process
For EN i, the arrival of content delivering request from user j is
Backlog evolution
For any average requested content data rate inside the capacity region, all queues must be stable, i.e.,
Notes: Add this one and last one between page 1 and page 3

## Slide 46
Case Study
Boundness
[O(V),O(1/V)] tradeoff
Notes: Add this page before the simulation results